## Slide 1
EE650 — Course Project Proposal
Risk-Sensitive CVaR-SMPC for
Autonomous Rover Navigation
in High-Variance, Deformable Terrain
Team TerraRisk
Sivaganesh B. • Sushil Krishna K. • Ramya Rasika S. R. • Kanishka S.
Indian Institute of Technology Kanpur

## Slide 2
The Problem
Two independent ways existing risk-aware planners fall short
1
Risk from appearance, not mechanics
LiDAR/camera risk maps encode elevation, roughness, slope — what the ground looks like.
Two visually-identical sand patches can have very different soil cohesion — one safe, one capable of entrapment. Geometry can't tell them apart.
Forces a bad choice: treat ambiguous terrain as safe (misses hazards) or hazardous (needlessly avoids safe routes).
2
Probability, not severity
Chance constraints bound how often a bad event happens — not how bad it is.
“Sinkage exceeds threshold only 5% of the time” treats a barely-exceeded case the same as a catastrophic, irreversible entrapment.
Real hazards are heavy-tailed: rare hidden soft-soil pockets are rare but severe — exactly what averages and simple chance bounds underweight.

## Slide 3
Where the Gap Sits
No existing work occupies the intersection
Terramechanics-based
physical sensing
[4] [5] — reactive, used
after slip begins
CVaR-based
risk-sensitive control
[9] — geometry-only
risk map (elevation)
This project:
physically-grounded CVaR-SMPC

## Slide 4
Literature Landscape
Three bodies of work, each solving one piece
Group | Papers | Gives us | Leaves out
Rover / off-road MPC | [1] [2] [3] | MPC as a practical, on-board control architecture | Terrain treated as deterministic or geometry-based, not an uncertain risk source
Terramechanics slip-sinkage | [4] [5] | Bekker-Wong models linking slip/sinkage/torque to soil cohesion & friction | Used reactively (after slip) for estimation/traction control — not inside a predictive planner
CVaR & risk-sensitive control | [6] [7] [8] | Chance constraints → CVaR as a coherent, convex, tractable risk measure | General-purpose theory — not specialized to terramechanics or rover navigation
Group
Papers
Gives us
Leaves out

## Slide 5
Closest Prior Work — Moon et al. [9]
Sampling-based MPC with CVaR risk assessment for off-road environments (2025)
What it does
Builds a recursive CVaR risk map from elevation data, updated as the rover moves
Uses a sampling-based (MPPI-style) controller — no differentiable cost or reference trajectory needed
Validated in simulation and on a real ground robot
Outperforms hybrid A* and standard MPC baselines on success rate and smoothness
What's missing
Risk map is elevation-only — pure geometry, no soil mechanics
No slip-sinkage dynamics modeled — the actual mechanism behind entrapment
No proprioceptive sensing of the rover's own wheel-soil interaction
CVaR reshapes a sampling distribution over geometric risk, not a physically-grounded dynamic model

## Slide 6
Proposed Pipeline
Physical sensing → soil estimate → tail-risk → control action
Physical Signals
slip • sinkage • torque • IMU
Bekker-Wong
Estimator
infers ĉ, φ̂, n̂
Predicted Sinkage
Distribution
over horizon N
CVaR-SMPC
penalizes tail severity
Control Action
steering • torque
This chain reuses standard CVaR math and standard Bekker-Wong physics — the novelty is the estimator + the coupling architecture connecting them.
Not novel: CVaR convex reformulation, SMPC structure, Bekker-Wong equations Novel: online proprioceptive soil estimator + the CVaR-SMPC coupling architecture

## Slide 7
Staged Build Plan
Matched to the course's three scheduled presentations
1
Known soil parameters
Assign soil params per patch from published tables. Validate the CVaR-SMPC controller in isolation from the sensing problem.
2
LiDAR/camera classification
Add coarse visual terrain classes → parameter ranges. Controller reasons under appearance-only uncertainty — reproduces prior work [9] as a fair baseline.
3
Physical sensing fused
Add proprioceptive signals with a recursive online estimator. Soil parameters — and CVaR-bounded risk — update in situ as the rover drives.

## Slide 8
Benchmarking Plan
Entrapment rate vs. path efficiency, across four controllers, one terrain generator
Deterministic
NMPC
No uncertainty modeling
Gaussian
SMPC
Light-tailed uncertainty only
Stage 2
(LiDAR/camera only)
Reproduces [9]'s sensing limit
CVaR-SMPC
(ours, Stage 3)
Physically-grounded tail-risk
Metrics
Entrapment rate • path efficiency • mission-completion time • safe traversal of visually-ambiguous terrain

## Slide 9
The One-Line Pitch
We couple physically-sensed terrain risk with tail-severity-aware (CVaR) predictive control — a combination the literature hasn't made — because appearance-based risk maps can't distinguish safe from unsafe terrain that looks the same, and probability-only risk bounds can't distinguish recoverable from catastrophic failure.
Thank you — questions welcome